## Slide 1
Shongket
Beyond the mobile coverage
A LoRa crew communication system with an optional phone companion
[Course / University] • [Student name(s)] • [Professor]

## Slide 2
The problem
SHONGKET | BEYOND THE MOBILE COVERAGE
02
Mobile messaging depends on infrastructure.
Small crews may still need short messages and location awareness where coverage is absent.
Project goal
An independent handheld network that can pass messages across nearby crew devices.

## Slide 3
System overview
SHONGKET | BEYOND THE MOBILE COVERAGE
03
Phone app
Read and compose through a nearby handheld over Bluetooth.
Handheld
ESP32, screen, keypad, GPS, and LoRa radio.
Crew mesh
Other handhelds receive and may relay new packets.
Bluetooth
LoRa
No internet service or central coordinator is required.

## Slide 4
A message can travel beyond one radio link
SHONGKET | BEYOND THE MOBILE COVERAGE
04
1 Send
The sender creates an encrypted packet.
2 Check
A neighbor accepts a valid new packet.
3 Relay
It waits briefly, then forwards once.
4 Confirm
A direct recipient returns an acknowledgement.
Duplicate copies are ignored. Relaying stops after three hops.

## Slide 5
Two ways to use Shongket
SHONGKET | BEYOND THE MOBILE COVERAGE
05
Handheld alone
Keypad and screen support messages, crew information, GPS radar, and device status. The phone is optional.
Phone companion
The app shows messages, crew, GPS, and radio health. It asks the bonded handheld to send; it does not use LoRa itself.

## Slide 6
Security and delivery meaning
SHONGKET | BEYOND THE MOBILE COVERAGE
06
Shared crew key
AES-128-CCM protects radio packets from outsiders without the key. Trusted crew devices share that key.
Honest status
Direct delivery requires a returning acknowledgement. Crew delivery only confirms that at least one peer accepted and relayed.
A relay is not proof that every crew member received a message.

## Slide 7
Validation and demonstration
SHONGKET | BEYOND THE MOBILE COVERAGE
07
Available evidence
Firmware and app test suites cover protocol, relay state, Bluetooth framing, UI input, and radar math.
Hardware observations
[ADD DEVICE PHOTOS AND OBSERVED RESULTS] Record two-device messaging, three-device relay, phone pairing, and GPS conditions.
No measured range or field reliability claim is made yet.

## Slide 8
Limits and next steps
SHONGKET | BEYOND THE MOBILE COVERAGE
08
Current limits
Up to 12 handhelds; three relay hops; RAM message history; shared crew key; no SOS or cloud archive.
Next steps
Document staged bench trials, attach real device evidence, then measure outdoor behavior under recorded conditions.
Shongket connects a standalone handheld, a small LoRa mesh, and an optional phone.